## Slide 1: CS 2080: Programming with UNIX
Dr. Armin moin, assistant professor
Quantum-Classical AI and Software Engineering (QAS) Lab
Department of computer science
University of Colorado colorAdo springs (uccs)
Summer 2024

## Slide 2: Lecture 2: BASIC Operating system concepts
Outline:
  What is an OS?
  Computer architecture and organization
  OS components
  Interrupts (hardware and software-based)
  Processes and multitasking
  Dual/multi modes of operation
  OS timer
  Principle-based Ethics
  Team formation and project ideation revisited

## Slide 3: Operating system (os)
A software system that manages a computer’s hardware resources and allocates those resources to programs.
Hardware resources: E.g., CPU, memory, I/O devices, and storage.
Examples of OSs: UNIX, other UNIX-Like OSs, such as GNU/Linux, Microsoft Windows, Apple’s Mac OS, TinyOS, ContikiOS

## Slide 4: The Cpu Instruction Cycles
Fetch
Decode
Execute

## Slide 5: Computer architecture and organization
Input Device
Memory Unit
Central Processing Unit (CPU)
Control Unit
Arithmetic/Logic Unit
Output Device
Figure inspired by Silberschatz et al. 2018
Registers

## Slide 6: A typical personal computer (PC) system
System bus
CPU
Memory
Controller
Disk Controller
USB Controller
Graphics adapter
Monitor
Printer
Keyboard
Mouse
Disks
Memory
Figure inspired by Silberschatz et al. 2018

## Slide 7: Device driver
An OS has typically a device driver for each device controller, which offers a uniform interface.
The CPU and the device controllers run in parallel and compete for memory cycles.
Memory controller: Orderly access to shared memory

## Slide 8: OS components
Kernel
Application programs
System programs
OS

## Slide 9: Mobile/IoT OS components
Kernel
Apps
System programs
OS
middleware

## Slide 10: Resource-constrained iot devices
Most of the resource-constrained Internet of Things (IoT) devices have no OS!

## Slide 11: Bootstrap
A small program stored within the computer hardware in firmware (e.g., BIOS / UEFI)
Initializes all aspects of the computer system when it is powered on: E.g., CPU registers, memory, and device controllers.
Bootstrap loads the OS kernel into the memory
Once the kernel is loaded, it can provide services to the system and its users

## Slide 12: Bootstrap
Some services are provided outside of the kernel by system programs loaded into the memory at boot time, known as system daemons, that run the entire time in the background.
  E.g., On Linux, systemd is the first system program that runs many other daemons.
The OS waits for an event, such as a hardware interrupt or a software interrupt (i.e., an exception, such as division by zero, or a system call).

## Slide 13: The interrupts mechanism
The interaction between the OS and the hardware
Sending a signal to the CPU via the system bus
CPU interrupted -> stops what it is doing -> immediately transfers execution to a fixed location (i.e., the starting address of the service routine for the interrupt) -> then, the CPU resumes its previously interrupted execution

## Slide 14: The interrupts mechanism
The device controller raises an interrupt by asserting a signal on the interrupt request line, the CPU catches the interrupt and dispatches it to the interrupt handler, and the handler clears the interrupt by servicing the device.
Nonmaskable and maskable interrupts (the latter can be turned off during the CPU’s critical processing)

## Slide 15: Multiprogramming and multitasking
Multiprogramming: The ability of an OS to run multiple programs. This increases the CPU utilization.
In a multi-programmed system, a program in execution is called a process.
A process is the unit of work in a system.

## Slide 16: Multiprogramming and multitasking
The OS keeps several processes in memory simultaneously. The CPU switches between them when it needs to wait; thus, it is never idle.
Multi-tasking: A logical extension of multiprogramming. The CPU switches among tasks frequently. The response time is fast. This satisfies the user.
CPU scheduling, disk storage (file system), memory management (virtual and physical), as well as process communication and synchronization need to be taken care of.

## Slide 17: Dual mode and multimode operation
Separating the execution of the OS code and the user-defined code by hardware support.
Kernel mode (superuser mode) vs. user mode
Mode bit: 0 (kernel), 1 (user)
Advantage: a malicious program cannot harm other programs or the OS

## Slide 18: Dual mode and multimode operation
The concept can be extended to multiple modes: e.g., the Intel processors with 4 protection rings
  Ring 0 = kernel, Rings 1 and 2 rarely used, Ring 3 = user
If the CPU supports virtualization, a separate mode is needed that indicates when the Virtual Machine Manager (VMM) is in control.
  user processes’ privileges < VMM privileges < the kernel’s privileges

## Slide 19: Virtualization vs. containerization
Virtualization: Running multiple OS instances on one machine – Hardware support
  E.g., VirtualBox or VMware
Containerization: Running a single OS instance on one machine with multiple user spaces to isolate processes (supports multi-tenancy) – Software support
  E.g., Docker

## Slide 20: The OS keeps watching
Checks for illegal instruction or illegal memory access (e.g., if the memory address is not in the user’s address space)
  The OS must terminate the program abnormally
  The same code as the user-requested abnormal termination
  Appropriate error message given and the memory dump written to a file

## Slide 21: The OS timer
The OS sets a timer before turning over control to the user mode.
The timer counts down until it reaches 0. In that case, it interrupts, and the control is automatically transferred to the OS. The OS may decide to give the process more time.
On Linux systems, the kernel configuration parameter HZ specifies the frequency of timer interrupts (i.e., the number of timer interrupts per second). Also, the kernel variable jiffies indicates the number of timer interrupts that have occurred since the system was booted.

## Slide 22: Principle-based ethics
Daniels Fund Ethics Initiative
  https://www.danielsfund.org/ethics/overview
  https://business.uccs.edu/resources/ethics
8 core principles

## Slide 23: Daniels Fund Ethics Initiative – Principle 1
Integrity
  Act with honesty in all situations

## Slide 24: Daniels Fund Ethics Initiative – Principle 2
Trust
  Build trust in all stakeholder relationships

## Slide 25: Daniels Fund Ethics Initiative – Principle 3
Accountability
  Accept responsibility for all decisions

## Slide 26: Daniels Fund Ethics Initiative – Principle 4
Transparency
  Maintain open and truthful communications

## Slide 27: Daniels Fund Ethics Initiative – Principle 5
Fairness
  Engage in fair competition and create equitable and just relationships

## Slide 28: Daniels Fund Ethics Initiative – Principle 6
Respect
  Honor the rights, freedoms, views, and property of others

## Slide 29: Daniels Fund Ethics Initiative – Principle 7
Rule of Law
  Comply with the spirit and intent of laws and regulations

## Slide 30: Daniels Fund Ethics Initiative – Principle 8
Viability
  Create long-term value for all relevant stakeholders

## Slide 31: Team formation
Talk to your peers
Form your semester project teams
Ideally, size 3

## Slide 32: Project ideation revisited
Now, you need to agree on one topic in your teams!
The topic that you choose does not matter that much
It just has to be somewhat interesting to you and related to this course
The way you apply the principles and practices you will learn to your project does matter!

## Slide 33: Questions?
See you!